## Slide 1: Desain & Pengelolaan Jaringan Konsep Dasar
Rochmad M Thohir Yassin

## Slide 2: Perkembangan Teknologi

## Slide 3: Tantangan IT
IT (jaringan komputer pada khususnya) diharapkan dapat memberikan solusi pada tren sekarang :
Bring Your Own Device (BYOD)
Online collaboration
Video communication
Cloud computing

## Slide 4: Tantangan IT (2)
IT juga diharapkan dapat memberikan solusi pada zaman tak terbatas (wilayah dan waktu serta perangkat) :

## Slide 5: How Important ?
Setiap sistem yang baik memerlukan desain yang baik pula
Implementasi yang baik tergantung pada desain yang dilakukan sebelumnya
Pada sistem informasi contohnya banyak metode untuk mendesain sistem hingga tahapan implementasi :
  Waterfall
  Prototyping
  Rapid Application Development
  Extreme Programming
Prinsip : Lebih baik mendesain tapi gagal daripada tidak sama sekali namun gagal juga

## Slide 6: Banyak Model dalam IT
  The Cisco Lifecycle Services (PPDIOO) model
  IT Infrastructure Library (ITIL)
  The Fault, Configuration, Accounting, Performance, and Security (FCAPS) model
    International Organization for Standardization (ISO)
  The Telecommunications Management Network (TMN) model
    Telecommunications Standardization Sector (ITU-T)
Semuanya mengatur agar implementasi sesuai dengan desain (tujuan awal)

## Slide 7: Cisco Model
Prepare
Optimize
Plan
Design
Implement
Operate

## Slide 8: Cisco Model (2)
The PPDIOO methodology begins with these three basic steps:
  Step 1: Identify customer requirements
  Step 2: Characterize the existing network and sites
  Step 3: Design the network topology and solutions
Once the design is defined, the implementation plan can be executed.
Identify customer requirements
Design the network
Characterize existing network
Prepare
Plan
Design

## Slide 9: Cisco Model (3)
The next three steps include:
  Step 4: Plan the implementation:
  Step 5: Implement and verify the design:
  Step 6: Monitor and optionally redesign:
Operate / Optimize
Plan the implementation
Monitor / Redesign
Implement and Verify
Design
Implement

## Slide 10: Cisco Model (4)
The implementation plan documentation should include the following:
  Network information
  Tools required
  Resources required
  Implementation plan tasks
  Verification tasks
  Performance measurement and results
  Screen shots and photos, as appropriate
The documentation creation process is not finished until the end of the project, when the verification information is added to it.

## Slide 11: McCabe Model
(McCabe, 2007)

## Slide 12: Complete McCabe Model Activity
(McCabe, 2007)

## Slide 13: Seberapa besar network yang akan di desain ?
Small network – Provides services for 1 to 200 devices.
Medium-sized network – Provides services for 200 to 1,000 devices.
Large network – Provides services for 1,000+ devices.

## Slide 14: Arsitektur apa yang hendak digunakan ?

## Slide 15: Hierarchy Network
Access layer – Provides workgroup or user access to the network.
Distribution layer – Provides policy-based connectivity.
Core layer – Provides fast transport between distribution switches.

## Slide 16: Access Layer
Layer 2 switching
High availability
Port security
QoS classification and marking and trust boundaries
Address Resolution Protocol (ARP) inspection
Virtual access control lists (VACLs)
Spanning tree
Power over Ethernet (PoE) and auxiliary VLANs for VoIP

## Slide 17: Distribution Layer
Aggregation of LAN or WAN links
Policy-based security in the form of access control lists (ACLs) and filtering
Routing services between LANs and VLANs and between routing domains (e.g., EIGRP to OSPF)
Redundancy and load balancing
A boundary for route aggregation and summarization configured on interfaces toward the core layer

## Slide 18: Core Layer
Provides high-speed switching (i.e., fast transport)
Provides reliability and fault tolerance
Scales by using faster, and not more, equipment
Avoids CPU-intensive packet manipulation caused by security, inspection, quality of service (QoS) classification, or other processes

## Slide 19: Cisco Enterprise Architecture

## Slide 20: Cisco Enterprise Architecture (2)

## Slide 21: Campus Architecture
Provides:
High availability with a resilient multilayer design and redundant hardware and software features.
Automatic procedures for reconfiguring network paths when failures occur.
Multicast to provide optimized bandwidth consumption.
Quality of Service (QoS).
Integrated security.
Flexibility to add IP security (IPsec) and MPLS VPNs, identity and access management, and VLANs to compartmentalize access.

## Slide 22: Data Centre Architecture
Provides head-office applications and services, such as security, Cisco IP Communications, and advanced application performance.
Integrates security, switching, network analysis, caching, and converged voice and video services into a series of integrated services routers in the branch.
Enterprises can centrally configure, monitor, and manage devices that are located at remote sites.

## Slide 23: Branch Architecture
Adaptive network architecture that supports the requirements for consolidation, business continuance, and security.
Redundant data centers provide backup services using synchronous and asynchronous data and application replication.
The network and devices offer server and application load balancing to maximize performance.
This solution allows the enterprise to scale without major changes to the infrastructure.

## Slide 24: Teleworker Architecture
Also called the Enterprise Branch-of-One, it allows enterprises to deliver secure voice and data services to remote SOHO offices over a broadband access service.
Centralized management minimizes the IT support costs.
Campus security policies are implemented using robust integrated security and identity-based networking services.
  Staff can securely log on to the network over an always-on VPN and gain access to authorized applications and services.

## Slide 25: Enterprise Composite Network Model
Building Access
Building Distribution
Core (Campus backbone)
Server Farm
Management
Edge
Distribution
E-Commerce
ISP A
Corporate Internet
Remote Access VPN
WAN
Frame Relay
/ ATM
PSTN
ISP B
Enterprise Campus
Enterprise Edge
Service Provider Edge

## Slide 26: Referensi
McCabe, D, J., 2007, Network Analysis, Architecture and Design, Morgan Kauffman.