## Slide 1: Teori aliran daya radial

## Slide 2: Teori aliran daya pada sistem distribusi
Aliran daya merupakan analisis yang sangat penting untuk mengetahui apakah kondisi sistem stabil atau tidak.
Tujuan utama dari analisis aliran daya adalah untuk mengetahui besar daya aktif dan reaktif yang mengalir di setiap saluran bersama dengan besarnya dan fase-fase dari tiap tegangan pada setiap bus sistem untuk kondisi pembebanan tertentu.
Secara umum sistem tenaga dibagi menjadi dua kategori:
Sistem transmisi
Sistem distribusi

## Slide 3
1. Transmission Systems

## Slide 4
IEEE 13 Node Test Feeder
2. Distribution Systems

## Slide 5
Sistem distribusi memiliki beberapa karakteristik yang berbeda dari sistem transmisi:
Memiliki struktur radial
Saluran yang tidak ditransposisikan
Memiliki jumlah node yang besar
Beban yang tidak seimbang, bersama dengan lateral satu fase dan dua fase
Rasio R/X yang tinggi
Fitur-fitur ini perlu diperhitungkan saat melakukan analisis aliran daya untuk sistem distribusi. Sistem distribusi perlu dianalisis berdasarkan tiga fase, tidak seperti sistem transmisi yang dapat dianalisis berdasarkan fase tunggal. Karena alasan ini. Metode Newton Raphson fase tunggal tradisional atau aliran daya untuk sistem ring tidak memadai untuk studi aliran daya distribusi [2].
[2] S. M. Moghaddas-Tafreshi, Elahe Mashhour, "Distributed generation modeling for power flow studies and a three-phase unbalanced power flow solution for radial distribution systems considering distributed generation," Electric Power Systems Research, Vol. 79, pp. 680-686, 2009.

## Slide 6
Metode yang biasa digunakan dalam analisis aliran daya untuk system distribusi adalah:
Modified Newton Rhapson
Implicit Z-bus Method
Modified Gauss-Seidel Method
Forward-backward Sweep method
Network Topology Based Method
etc

## Slide 7: I. FORWARD-BACKWARD ITERATIVE TECHNIQUE
1. Linear Network
1
2
3
4
5
I12
I23
I34
I45
I2
I3
I4
I5
ZL2
ZL3
ZL4
ZL5
Z12
Z23
Z34
Z45
+
Vs
-
Figure 1.1 Linear Network
Linear network, load is Constant load impedance.
From that figure:
Assuming that all of impedance and all of the load is known.

## Slide 8
FORWARD SWEEP
Start from the end of the node.
Assuming is known (Initial guest).
Look at the end of the node.
Calculate :
1
2
3
4
5
I12
I23
I34
I45
I2
I3
I4
I5
ZL2
ZL3
ZL4
ZL5
Z12
Z23
Z34
Z45
+
Vs
-

## Slide 9
Using Kirchoff’s current law:
Continue until calculate .
Compare and to know the error.
If error is less then tolerance its mean the solution is achieved Else
Continue to backward sweep.
1
2
3
4
5
I12
I23
I34
I45
I2
I3
I5
ZL2
ZL3
ZL4
I4 ZL5
Z12
Z23
Z34
Z45
+
Vs
-

## Slide 10
BACKWARD SWEEP
Calculate V2:
And then calculate
using:
Continue until
1
2
3
4
5
I12
I23
I34
I45
I2
I3
I4
I5
ZL2
ZL3
ZL4
ZL5
Z12
Z23
Z34
Z45
+
Vs
-

## Slide 11: 2. Non Linear Network
The linear network of figure 1.1 is modified to a non linear network by replacing all of constant load impedance by constant complex power load.
S5
1
2
3
4
5
I12
I23
I34
I45
I2
I3
I4
I5
Z12
Z23
Z34
Z45
S4
S3
S2
+
Vs
-
Figure 1.2 Non Linear Network
FORWARD SWEEP
The differences of calculation between linear network and non linear network is how to calculate

## Slide 12
Assuming
is known (Initial guest).
Look at the end of the node.
Calculate :
S5
1
2
3
4
5
I12
I23
I34
I45
I2
I3
I4
Z12
Z23
Z34
Z45
S4
S3
S2
+
Vs
-

## Slide 13
Using Kirchoff’s current law:
Continue until calculate .
Compare and to know the error.
If error is less then tolerance it’s mean the solution is achieved Else
Continue to backward sweep.
S5
1
2
3
4
5
I12
I23
I34
I45
I2
I3
I4
Z12
Z23
Z34
Z45
S4
S3
S2
+
Vs
-

## Slide 14
BACKWARD SWEEP
Calculate V2:
And then calculate
using:
Continue until
S5
1
2
3
4
5
I12
I23
I34
I45
I2
I3
I4
Z12
Z23
Z34
Z45
S4
S3
S2
+
Vs
-

## Slide 15: EXAMPLE:
1
2
3
I12
I23
I2
I3
Z12
Z23
S3
S2
+
Vs
-
Impedance data:
Load data:

## Slide 16: SOLUTION:
FORWARD SWEEP
Step 1: Assume
.
1
2
3
I12
I23
I2
I3
Z12
Z23
S3
S2
+
Vs
-

## Slide 17: Step 2:
Look at the end of the node.
Calculate
Step 3:
Calculate load current at node 2:
1
2
3
I12
I23
I2
I3
Z12
Z23
S3
S2
+
Vs
-

## Slide 18
Step 4:
Calculate current in line segment 1-2:
Step 5:
Compute voltage at source node( :
1
2
3
I12
I23
I2
I3
Z12
Z23
S3
S2
+
Vs
-

## Slide 19: Step 6:
Check the error.
Usually the error tolerance is
1
2
3
I12
I23
I2
I3
Z12
Z23
S3
S2
+
Vs
-

## Slide 20: BACKWARD SWEEP
Step 7:
Calculate :
Step 8:
Calculate :
1
2
3
I12
I23
I2
I3
Z12
Z23
S3
S2
+
Vs
-

## Slide 21: Go to step 1 to calculate
using updated
And repeat until error tolerance is less than
One line usually used in Power system
G
1
2
3
S2
S3
1
2
3
I12
I23
I2
I3
Z12
Z23
S3
S2
+
Vs
-

## Slide 22: 3. General Feeder
9
11
Source node
1
2
3
4
5
6
7
8
10
12
13

## Slide 23: The ladder iterative technique for
the feeder would proceed as
follows:
Assume three-phase voltages at the end nodes (6, 8, 9, 11, and 13). The usual assumption is to use nominal voltages.
Starting at Node 13, compute the
node current (load current plus
current capacitor if present).
With this current, apply Kirchhoff’s voltage law (KVL) to calculate the node voltages at 12 and 10.
Node 10 is referred to as a ”junction” node since laterals branch in two directions from the node. For this feeder go to Node 11 and compute the node current.
9
11
Source node
1
2
3
4
5
6
7
8
10
12
13

## Slide 24: Use that current to compute the
voltage at Node 10. This will be referred to as “the most recent voltage at Node 10”.
5. Using the most recent value of the
voltage at
current at
Node 10, the node Node 10 (if any) is
computed.
6. Apply Kirchhoff’s current law (KCL) to determine the current
flowing from Node 4 toward Node 10.
Compute the voltage at Node 4.
Node 4 is junction node. An end node downstream from Node 4 is selected to start the forward sweep toward Node 4.
Select Node 6, compute the node current, and then compute the voltage at junction Node 5.
9
11
Source node
1
2
3
4
5
6
7
8
10
12
13

## Slide 25: 10. Go to downstream end node 8.
Compute the node current and then the voltage at junction Node 7.
Go to downstream end node 9.
Compute the node current and then the voltage at junction Node 7.
Compute the node current at Node 7 using the most recent value of the Node 7 voltage.
Apply KCL at Node 7 to compute
the current flowing on the line segment from Node 5 to Node 7.
Compute the voltage at Node 5.
Compute the node current at Node 5
Apply KCL at Node 5 to determine the current flowing from
Node 4 toward Node 5.
Compute the voltage at Node 5.
Compute the node current at Node 5.
9
11
Source node
1
2
3
4
5
6
7
8
10
12
13

## Slide 26
19. Apply KCL at Node 5 to
determine the current flowing from Node 3 to Node 4
20. Calculate the voltage at Node 4.
21. Compute the node current at node 4.
Apply KCL at Node 3 to compute the current flowing from Node 2 to Node 4
Calculate the voltage at Node 2
Compute the node current at node 2
Apply KCL at Node2.
Calculate the voltage at Node 1.
Compare the calculated voltage at
Node11 to the specified source voltage.
28. If not within tolerance, use the
specified source voltage and the
9
11
Source node
1
2
3
4
5
6
7
8
10
12
13

## Slide 27: forward sweep current flowing
from Node 1 to Node 2, and
compute the new voltage at Node 2.
29. The backward sweep continues,
using the new upstream voltage and line segment current from the
forward sweep to compute the new downstream voltage.
The backward sweep is completed
when new voltage at all end nodes have been completed.
This completes the first iteration.
Repeat the forward and backward sweeps until the calculated voltage at the source is within a specified tolerance of the source voltage.
33. Continue the forward and backward sweeps until the calculated voltage at the source is
9
11
Source node
1
2
3
4
5
6
7
8
10
12
13

## Slide 28: within a
specified tolerance of
source voltage.
34. At this point the voltages are
known at all nodes, and the current flowing in all line segments are known. An output report can be
produced giving all desired results.
9
11
Source node
1
2
3
4
5
6
7
8
10
12
13
Reference:
1. William H. Kersting, “ Distribution System Modeling and Analysis” CRC PRESS 2002 . Pages 269-290